## Slide 1: Residential Subdivision: Jordan Cove Waterford’s LID Subdivision, 15 Years later
Michael Dietz, Ph.D. University of Connecticut Center for Land Use Education and Research (CLEAR)
Rockfall Foundation Symposium
March 22, 2018

## Slide 2: Jordan Cove project
Ten year project (1995-2005)
US EPA/CT DEEP funded
Led by Dr. Jack Clausen at UConn
Outreach by CLEAR
http://jordancove.uconn.edu
Funded in part by the Connecticut Department of Energy and Environmental Protection through a United States Environmental Protection Agency Clean Water Act Section 319 Nonpoint Source Grant

## Slide 3
Jordan Cove Urban Watershed Project
Objective was to investigate:
  -Impacts of residential construction
  -Efficiency of a group of selected BMPs
  -Effectiveness of a community educational program

## Slide 5
  Water quantity and quality measured downstream of 3 different subdivisions

## Slide 6: Traditional subdivision

## Slide 7: LID Subdivision
Cluster layout with shared driveways
Open space and low-mow area
Bioretention cul-de-sac
Grassed swales
Rain gardens
Pervious roadway

## Slide 8
Bioretention cul-de-sac

## Slide 9: Rain gardens

## Slide 10: Pervious road and grassed swales

## Slide 12: Runoff depth

## Slide 13: Side note on swales
Swales in right-of-way and managed by homeowners are subject to the way homeowners manage their lawns!

## Slide 14: Behavior Surveys
Pets, lawn care (targeting fertilization practices), leaves, gutters
Given to all residents (control, traditional, LID)
LID residents received one-on-one education from university personnel, free soil testing, demonstrations

## Slide 15
Initial surveys: ALL RESIDENTS said that they did not fertilize their lawn…but the evidence showed otherwise

## Slide 16: Jordan Cove survey results
NO SIGNIFICANT DIFFERENCES IN BEHAVIOR AMONG WATERSHEDS or ACROSS YEARS
High intensity education methods DID NOT WORK here
Fortunately, stormwater and pollutant export and were much lower from the LID watershed

## Slide 17: Social factor - lesson learned
People end up acting like their neighbors
Social norms theory

## Slide 18
MAR

## Slide 19: Jordan Cove
Uni-EcoStone® paver road and driveways
2002
2005

## Slide 20: 2018

## Slide 21: Paver road
Clogged, but still functions (1 inch per hour)
Integrity of road surface (almost 20 years old!) is amazing

## Slide 22: Some settling and turf dams along flush curb edge

## Slide 23: Driveway pavers still infiltrating

## Slide 24: Rain gardens
8 originally installed – 6 still exist and are functional
Social norms theory??

## Slide 26: Cul-de-sac bioretention

## Slide 27: Cul-de-sac bioretention
Either make all grass, or plant a small number of large trees
Makes maintenance easier

## Slide 28: Summary
Social factors are still important
Most rain gardens still in place
No maintenance done on paver road, but it is still functioning
Some settling of road prevents water from getting into swales

## Slide 29: 2005 take home message: (in spite of what people do…) http://jordancove.uconn.edu
LID works!

## Slide 30: 2018 take home message: (in spite of what people do…) http://jordancove.uconn.edu
LID (mostly) STILL works!

## Slide 31: Thank You! michael.dietz@uconn.edu

## Slide 32: Site preparation
If soil is highly compacted, you need to remove, or loosen and aerate
  Compacted soil will cause a rain garden or bioretention area to fail
Someone “in the know” needs to be on site for installation