## Slide 1: Soil-Based Wastewater Treatment and the Challenges of Climate Change
Jose A. Amador
Laboratory of Soil Ecology and Microbiology University of Rhode Island
Kingston, RI

## Slide 2
OVERVIEW
OWTS
Climate change
Effects
What to do?

## Slide 3: OWTS: A PRIMER

## Slide 4: What is an Onsite Wastewater Treatment System (OWTS)?
AKA:
  Septic system
  Individual sewage disposal system (ISDS)
Effectively treat wastewater
Two flavors:
  Conventional
  Advanced
Performance generally not regulated after installation
All underground (out of sight, out of mind…)

## Slide 5
Two flavors of OWTS:
Conventional
Advanced

## Slide 6: Drainfield

## Slide 7: What’s in Effluent?
Suspended solids
Organic C (BOD)
Pathogens
Phosphorus & Nitrogen
  Ammonium/Nitrate
Emerging pollutants
Anoxic/Oxic

## Slide 8: What Do They Do?
Keep wastewater away from people
Groundwater recharge/stream flow
Remove
  Suspended solids
  C, N, P
  Emerging pollutants
  Pathogens

## Slide 9: How Do They Do It? – The Tank

## Slide 10: How Do They Do It? – The Drainfield

## Slide 11: Larger Context

## Slide 12: Part of Water Infrastructure

## Slide 13: Source of Contaminants

## Slide 14: Climate Change

## Slide 15
Sea level rise? Drier? Wetter? Warmer?

## Slide 17
IPCC (2013)
Sea Level is Rising

## Slide 18
Rising Faster in Some Areas
IPCC (2013)

## Slide 19
Temperature is Increasing
IPCC (2013)

## Slide 20
Precipitation Patterns Are Changing
IPCC (2013)
Precipitation will change

## Slide 21
Probability of Extreme Events is Increasing
Phenomenon & direction of trend | Early 21st century | Late 21st century
Warmer and/or fewer cold days and nights over most land areas | Likely (66 - 100%) | Virtually certain (99 - 100%)
Warmer and/or more frequent hot days and nights over most land areas | Likely (66 - 100%) | Virtually certain (99 - 100%)
Warm spells/heat waves. Frequency and/or duration increases over most land areas | Not assessed | Very likely (90 - 100%)
Heavy precipitation events. Increase in the frequency, intensity, and/or amount of heavy precipitation | Likely (66 - 100%) over many land areas | Very likely (90 - 100%) over most of the mid-latitude land masses and over wet tropical regions
Increases in intensity and/or duration of drought | Low confidence | Likely (66-100%) on regional to global scale
Increased incidence and/or magnitude of extreme high sea level | Likely (66 -100%) | Very likely (90 - 100%)
Adapted from IPCC (2013)

## Slide 23: Potential Effects

## Slide 24
OWTS
Sea level rise
Increased temperature
Change in precipitation

## Slide 26
SLR: Acute Effects

## Slide 27
Photo: D. Potts
Westport, CT
SLR: Acute Effects

## Slide 28
SLR & Rising Water Tables

## Slide 29
<1’
SLR: Chronic Effects
Reduced OWTS function under elevated sea level/groundwater conditions

## Slide 30
Chart: 
| 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0
Y-Value 1 | 12.77 | 12.45 | 12.14 | 11.84 | 11.56 | 11.29 | 11.03 | 10.78 | 10.54 | 10.31 | 10.08 | 9.87 | 9.67 | 9.47 | 9.28 | 9.09 | 8.92 | 8.74 | 8.58 | 8.42 | 8.26 | 8.11 | 7.97 | 7.83 | 7.69 | 7.56
[O2] (mg/L)
T (oC)
HIgher Temperature: Less Oxygen Available

## Slide 31
Higher Temperature: More Oxygen Use
Davidson et al. (1998)

## Slide 32
Changes in Soil Water: +/- Microbial Activity
Davidson et al. (1998)

## Slide 33
Changes in Soil Water:
Aerobic vs. Anaerobic Processes
Linn and Doran (1984)

## Slide 34
Hypothesized Effects of Climate Change
Property/Process |  | 
Volume |  | 
Strength |  | 
Oxygen |  | 
Respiration |  | 
Nitrification |  (?) |  (?)
Denitrification |  (?) |  (?)
Xenobiotic degradation |  | 
S oxidation |  | 
P retention |  | 
Pathogen removal |  | 

## Slide 35: Impact of Climate Change on Drainfields
Intact Soil Core Mesocosms
Three Drainfield Types:
  Pipe & stone – P&S
  Shallow narrow – SND
  Shallow narrow – GeoMat
Climate Conditions:
  Present climate: 70oF
  Climate change: 77oF; Water table up 1 ft

## Slide 37
Oxygen

## Slide 38
Fecal coliform bacteria

## Slide 39
Phosphorus

## Slide 40: Quantifying Rising Water Tables

## Slide 44: Quantifying Storm Impacts
Model different storm conditions along southern RI coast…
Count number of septic systems affected
Notes: What if a ____ storm hits the coast, how many systems would be affected?
Severity of impact depends on location (storm surge damage), as well as length of inundation during storm/flood event (elevation)

## Slide 45: Summary of Storm Impacts (no SLR)
Require repairs!

## Slide 46: Overall Impacts on Septic Systems
Notes: Update #s

## Slide 47: What to do?

## Slide 48
Manage stormwater & wastewater
Use low impact development (LID) measures
Use green infrastructure practices
Increase wetland setbacks and buffers
Adaptation and mitigation
Think integrated water management:

## Slide 49
Protect areas that collect and infiltrate stormwater
Minimize disturbance (maintain natural hydrology)
Uncompact soil – restore to original soil hydrologic conditions
Think integrated water management:

## Slide 50
Adapt existing technologies
Improve component-based treatment efficiency
Develop new technologies
Incorporate moisture managementt into treatment trains (i.e. flow equalization, timed-dosing)
Adaptation and mitigation
OWTS Manufacturers:

## Slide 51
Map at-risk areas – set priorities
Develop risk-based policy and regs
Require accountability for treatment and O&M performance
Adaptation and mitigation
Regulators:

## Slide 52
Manage soil moisture:
  Promote timed-dosing and flow equalization
Promote shallow wastewater dispersal
  More biochemically reactive soil
  Maximize vertical separation distance
  Maximize retention time
In wetter areas

## Slide 53
Soil treatment area dispersal?
Landscape irrigation
Wastewater recycling and reuse
Advanced treatment will become more important
In drier areas:

## Slide 54
Rhode Island high risk flood and erosion areas
Repair systems - holding tanks, if 50 ft. to eroded feature; denitrification technologies otherwise
Example: Mitigating Acute Effects in East Coast Storm Impact Zones
Matunuck, RI
Greenhill, RI
(post Hur. Sandy Oct. 2012)

## Slide 55
Photo: Brian Moore, RIDEM
Hurricane Sandy Damage - Atlantic Ave., Misquamicut, RI
Use risk-based BMPs in designs -
Watertight lids
Anti-floatation and strapping
on tanks and components
Stone BSF enclosures
Elevated control panel boxes

## Slide 56
Isaac Cordal, Follow the Leaders, Berlin, Germany, 2011